## Slide 1
Presented By:
Ndimele, P.E. ; Mekuleyi, G. O. and Nweze,J.
Department of Fisheries
Faculty of Science
Lagos State University
October, 2017.
Heavy Metal Concentrations in Chrysichthys nigrodigitatus and Eichhornia crassipes from Ologe Lagoon and its Tributaries in Lagos, Nigeria

## Slide 2: OUTLINES
Introduction
Materials and Methods
Results
Discussion
Conclusion

## Slide 3: INTRODUCTION
Most Nigeria’s Lagoons are prone to various sources of pollution such as :
Domestic wastes, industrial wastes and chemicals from farm etc
Non-biodegradable nature of heavy metals made it one of the most notorious burdens to aquatic ecologists (Ndimele et al.,2010)
While some heavy metals such as zinc, copper, manganese and iron played significant roles in the metabolic activities of aquatic and terrestrial organisms,
Metals like lead, cadmium, arsenic and mercury, have been reported to be toxic even at low concentrations (Whenu and Mekuleyi,2017)

## Slide 4: MATERIALS AND METHODS
Study area
Ologe Lagoon is a freshwater body
It has a surface area of about 64.5 km2
Lies between latitude 6°27’N and 6°30’N and longitudes 3°02’E and 3°07’E on the equator (Kumolu-Johnson et al.,2010)
Links up to Atlantic ocean via Badagry creek and the Lagos harbour (Ndimele et al., 2011).

## Slide 5: COLLECTION OF SAMPLES,DIGESTION &METALS ANALYSIS
Water, sediment, fish and macrophyte were collected monthly from six sampling stations.
Samples were collected and treated according to FEPA and APHA standard methods.
Sediment was digested using the Nitric-peroxide acid digestion procedure.
2 grams of sediment was weighed on the Mettler balance (DM-11-K)
To sample put in a beaker, 10ml of nitric acid and 5ml of hydrogen peroxide were added and heated on a hot plate for about forty five minutes until the solid dissolved and the volume of contents was reduced to about 5 ml.
Contents were then filtered through a 0.45-μ Millipore membrane filter paper transferred quantitatively to a 50ml volumetric flask by adding de-ionized water and analysed for heavy metals in an AAS.

## Slide 6: COLLECTION &DIGESTION OF SAMPLES (contd)
Contents were filtered through a 0.45-μ Millipore membrane filter paper transferred quantitatively to a 50ml volumetric flask by adding de-ionized water and analysed for heavy metals in an AAS(Buck scientific 210 VGP model, USA )
Chrysichthys nigrodigitatus was dissected with high quality corrosion resistance stainless knife
2 gram of the samples were weighed on the Mettler balance (DM-11-K)
By using paper tape, samples were put in the beaker labelled with the various fish organs
Ten(10)ml of nitric acid and 5ml hydrogen peroxide were added to each of the organs &heated in the fume chamber.

## Slide 7: RESULTS
SEASON | pH | ALKALINITY (MG/L) | SALINITY (PPT) | HARDNESS | TURBIDITY (NTU)
WET | 5.763± 0.349a | 34.333±1.703a | 0.003±0.004a | 1353.167±1150.547 a | 24.750±5.511 a
DRY | 6.161±0.185a | 33.111±2.383a | 0.002±0.003a | 112.000±26.891 b | 19.556±1.281 b
Table 1: Seasonal variation of physico-chemical parameters

## Slide 8: RESULTS (contd)
TABLE 2: SEASONAL VARIATION OF HEAVY METALS IN WATER COLUMN
SEASONS | Fe (mg/l) | Zn (mg/l) | Cu (mg/l) | Pb (mg/l) | Cd (mg/l)
WET | 0.5255±0.1033 a | 0.0318±0.01582 a | 0.0889±0.2208 a | 0.0365±0.02037 a | 0.0106±0.00505 a
DRY | 0.7010±0.18410 a | 0.0193±0.00867 a | 0.0053±0.00267 a | 0.0332±0.02211 a | 0.0132±0.00578 a

## Slide 9: RESULTS (contd)
WET | 1257.891±431.646a | 6.982±1.530 a | 28.153±11.086 a | 9.785±1.656 a | 0.731±0.138 a
DRY | 2288.269±329.693 b | 23.461±1.4667 b | 0.568±0.109 b | 8.677±2.089 a | 0.4611±0.138 a
SEASONS | Fe (mg/kg) | Zn (mg/kg) | Cu (mg/kg) | Pb (mg/kg) | Cd (mg/kg)
TABLE 3: SEASONAL VARIATION OF HEAVY METALS IN SEDIMENT

## Slide 10: RESULTS (contd)
SEASONS | Fe (mg/kg) | Zn (mg/kg) | Cu (mg/kg) | Pb (mg/kg) | Cd (mg/kg)
WET | 139.710 ±13.261 a | 129.774±51.129 a | 9.965±3.787 a | 18.602±2.895 a | 1.513±0.307 a
DRY | 618.248±236.423 b | 87.144 ±36.229 b | 0.466±0.095 b | 7.536±1.242 b | 0.605±0.163 a
TABLE 4: SEASONAL VARIATION OF HEAVY METALS IN PLANT (Eichhornia crassipes)

## Slide 11
SEASONS | Fe (mg/kg) | Zn (mg/kg) | Cu (mg/kg) | Pb (mg/kg) | Cd (mg/kg)
WET | 9.292±9.292a | 0.753±0.753 a | 13.564±13.564 a | 2.205 ±2.205 a | 0.147 ±0.147 a
DRY | 22.192±7.1338b | 25.354±16.268b | 0.154±0.1322b | 1.717±0.0736 a | 0.192±0.102 a
TABLE 5: SEASONAL VARIATION OF HEAVY METALS IN FISH (Chrysichthys nigrodigitatus)
RESULTS (contd)

## Slide 12
STATIONS | pH | ALKALINITY (mg/l) | SALINITY (ppt) | HARDNESS | TURBIDITY (NTU)
AGBARA | 5.81±0.3074a | 29.50±3.403 a | 0.02±0.004 a | 250.00±121.650 a | 30.25±13.413 a
OLOGE JETTY | 6.59±0.37a | 40.00±5.291 b | 0.01±0.001 a | 106.67±52.679 b | 16.67±1.856 b
IMUDE | 5.69±1.04a | 34.67±1.764 ab | 0.01±0.003 a | 60.67±9.955 ab | 29.67±3.065 a
MOROGBO | 5.66±0.38a | 33.50±2.500 ab | 0.02±0.003 a | 264.00±164.657 ac | 19.75±12.733b
ERA | 6.56±0.31a | 30.00±1.155 ac | 0.01±0.002 a | 4766.67±4610.947c | 25.67±3.180 c
UNDERBRIDGE | 5.56±0.63a | 36.00±3.367 bc | 0.01±0.002 a | 97.00±33.838 bc | 14.25±3.038 bc
TABLE 6: SPATIAL VARIATION IN PHYSIOCHEMICAL PARAMETERS.
RESULTS (contd)

## Slide 13
STATIONS | Fe (mg/l) | Zn (mg/l) | Cu (mg/l) | Pb (mg/l) | Cd (mg/l)
AGBARA | 0.480 ± 0.110a | 0.012±0.011a | 0.095± 0.055a | 0.088± 0.054a | 0.011± 0.007a
OLOGE JETTY | 0.795 ± 0.298 a | 0.015±0.015a | 0.056± 0.049a | 0.000± 0.000a | 0.013± 0.013a
IMUDE | 0.573 ± 0.201 a | 0.017±.012a | 0.026± 0.020a | 0.410± 0.041a | 0.012± 0.017a
MOROGBO | 0.577± 0.134 a | 0.058±0.045a | 0.034± 0.026a | 0.052± 0.033a | 0.009± 0.008a
ERA | 0.430± 0.210 a | 0.031±0.031a | 0.065± 0.056a | 0.007± 0.007a | 0.000± 0.000a
UNDERBRIDGE | 0.260± 0.067 a | 0.025±0.016a | 0.049± 0.040a | 0.000± 0.000a | 0. 020±0.010a
TABLE 7: SPATIAL VARIATION OF HEAVY METALS IN WATER COLUMN
RESULTS (contd)

## Slide 14
STATIONS | Fe (mg/kg) | Zn (mg/kg) | Cu (mg/kg) | Pb (mg/kg) | Cd (mg/kg)
AGBARA | 1739.625±823.787a | 13.082±5.287a | 12.683±11.341a | 7.051± 1.177a | 0.662±0.229a
OLOGE JETTY | 1833.812±456.592b | 15.011±5.712ab | 14.941±14.415b | 5.982± 2.298b | 0.342±0.171a
IMUDE | 1874.238±595.467ab | 17.291±5.304ac | 9.997±7.679a | 11.797±2.684ab | 0.538±0.309a
MOROGBO | 1157.1783± 419.425ac | 13.732±4.896b | 7.445± 6.547b | 8.821± 3.978ac | 0.738±0.285a
ERA | 431.100± 109.750ad | 3.773±2.553bc | 17.500±16.150ab | 7.653±1.980ac | 0.313±0.113a
UNDERBRIDGE | 2560.329± 1101.323c | 16.484±5.826c | 35.208±33.785ac | 12.897±4.220c | 0.880±0.214a
TABLE 8: SPATIAL VARIATION OF HEAVY METALS IN SEDIMENT

## Slide 15
STATIONS | Fe (mg/kg) | Zn (mg/kg) | Cu (mg/kg) | Pb (mg/kg) | Cd (mg/kg)
AGBARA | 378.011±280.683a | 156.048±86.169a | 5.321±4.602a | 10.323±4.898 | 0.769±0.371
OLOGE JETTY | 954.837±658.007b | 75.5160±64.570b | 0.443±0.228b | 4.044±2.135 | 0.243±0.243
IMUDE | 91.526±37.259ab | 82.670±45.481ab | 3.470±3.322a | 9.292±5.681 | 0.847±0.571
MOROGBO | 247.969±164.255ac | 15.412±6.648ac | 0.766±0.337a | 8.454±3.392 | 0.576±0.367
ERA | 64.975±64.975c | 11.075±11.075c | 1.038±1.038a | 6.938±6.938 | 0.500±0.500
UNDERBRIDGE | 134.503±48.217cd | 74.430±55.833cd | 5.591±5.376a | 10.289±5.679 | 1.001±0.452
TABLE 9: SPATIAL VARIATION OF HEAVY METALS IN PLANT(Eichhorniacrassipes)
RESULTS (contd)

## Slide 16: DISCUSSION
Physiochemical Parameters in water column
The pH value is ideal for Fish growth and survival (Boyd, 1981, WHO)
This agrees with the observation made by Usoroet al (2013) of Iko river
The Turbidity values exceeded considerable limits for Fresh water body (FEPA, 1991).
This correlate with the turbidity reported by Archana Gupteet al (2013)
The mean value of hardness in this study was considered very high for a Lagoon (Tucker .1993)
Therefore, Ologe is considered hard water according to Mairs (1966) report
The high values of alkalinity in the wet season which is closely related to that in dry season obtained in Ologe lagoon
suggest that lagoon sediment or floor contain high level of carbonated deposits as was reported by Boyd (1981)
This corresponds with work done by Ahmed Set al (2015)while the order of metals in the sediments was Fe > Cu >Pb> Zn >Cd

## Slide 17: DISCUSSION (contd)
  Heavy metals in water column, Sediment, plant and Fish species:
All values of Heavy metals in water sample during this study are within the FEPA limits for heavy metals surface waters which are CU (<1), Fe (<20), Zn (<1), Pb (<1) and Cd(<1).
The increased order Fe>Pb> Cu > Zn > Cd corresponds with work done by Ahmed et al .(2015)
The seasonal Variation of heavy metals in sediment which was reported in Table 3. exceeded the FEPA limits for heavy metals in surface waters in mg/l except cadmium with lowest value 0.4611±0.138 in dry season. This was lower than those reported by Whenu and Mekuleyi(2017) and Kumolu-Johnson et al.(2012)
Both sediment and Eichhornia crassipes had high seasonal heavy metal above FEPA Limit.

## Slide 18: DISCUSSION (contd)
The mean concentration of heavy metals in Fish (Chrysichthys nigrodigitatus) exceeded the limit of FEPA
. This corresponds to a similar work done by Adeosun et al. (2010) where the concentration of zinc is significantly higher in bone of C. nigrodigitatus than all other tissue of same species examined.

## Slide 19: CONCLUSION
The study showed that water quality variables and heavy metal content of the water bodies can still sustain fish
But it may be harmful to the inhabitance of the Community
Therefore, efforts should be made by all users of the water bodies to take caution on discharging untreated wastes into these aquatic ecosystems.

## Slide 20
Thank you for listening