## Slide 1: Cloud Attenuation Modelling for Satellite Network Links Performance Improvement
O. M. Adewusi, T. V. Omotosho, M. L. Akinyemi, O. O. Ometan, S. A. Akinwunmi and A. A. Umar
FoSC 2017
Department of Physics
Lagos State University

## Slide 2: OUTLINE
Introduction
Scenario Illustration
Comparisons of The Foundation Cloud Models
Station Cloud Cover
Station Radiometric Data Acquisition and Analysis
Cloud Attenuation Modelling
Conclusion
Future Work
References

## Slide 3: Introduction -1
Observations show satellite services unavailability in most of the tropical region as southwest Nigeria is currently above the allowed 1% outage percentage and the tropical region cloud cover is averagely 70%, [2, 3]. The percentage of cloud attenuation in the total atmospheric hydrometeors' attenuation effects is high, and moreover cloud is more persistent in the tropical region.

## Slide 4
Figure 1: Atmospheric Layers and Clouds (Bertrand, 2002).

## Slide 5
Figure 2: Cloud Types and Classification (Warren and Hans, 2002)

## Slide 6
Modulator
Demodulator
Indoor Unit
Figure 3.0: Schematic Station Hydrometeor Attenuation Measurement Set up

## Slide 7: Introduction - 2
Low clouds – Stratus (St), Cumulus (C) Stratocumulus (Sc), Cumulonimbus (Cb), and Nimbostratus (Ns) have bases in the atmospheric boundary layer less than 2km above the earth surface;
Middle or alto clouds – Altostratus (As), Altocumulus (Ac) are clouds with bases 2 – 6km above the surface;
High or cirro clouds – cirrus (Ci), cirrocumulus (Cc) and cirrostratus (Cs) are clouds with bases between 6km above the surface and the tropopause [5] .

## Slide 8: Introduction - 3
The effects of suspended water droplets (SWD) and suspended ice crystal (SIC) which constitute clouds are major concern in the design and successful operation of satellite communication system; at frequencies above 10GHz.
Thus, for low-availability satellite services such as VSAT and USAT, at high frequencies, deep fades may occur, particularly in the tropics, due to higher probability of occurrence of cloud cover [2, 3].

## Slide 9: Introduction - 4
The general objective of cloud models (Table 1) is to accurately estimate cloud liquid water amount for determination of amount of cloud attenuation along a satellite earth-space transmission path.
Numerous cloud models have been independently developed over the last eight decades based on Rayleigh scattering and Mie absorption theories, using empirical data, [4].

## Slide 10: Table 1: A Comparative List of the Cloud Models.

## Slide 11: Table 1: A Comparative List of the Cloud Models (2/3).

## Slide 12: Table 1: A Comparative List of the Cloud Models (3/3).

## Slide 13: The Station’s Cloud Cover
The cloud cover of a station is a graphical relationship that shows the monthly variation of the percentage of cloud amount on the station’s sky dome, thus daily total cloud amount need be accurately estimated by visual method or by an efficient cloud estimating instrument, and the monthly average total is computed through each year.

## Slide 14: The Station’s Cloud Cover -2
Cloud measurement method includes satellites cloud observations on one hand and visual measurement of cloud from the earth’s surface stations on the other.
On the visual measurement, each assessment view of the total amount of cloud entails determination of cloud amount in cloud layers between the cloud base and maximum vertical distance visible for each of the four sky quadrants during each of the fixed daily observation times.

## Slide 15: The Station’s Cloud Cover -3
Table 2 shows typical weekly record of the visual cloud data and Figure 4 shows the visual cloud cover result for.
Table 2: Typical Visual Cloud Cover Weekly Record

## Slide 16
FIGURE 4: OTA - CU CLOUD COVER

## Slide 17: The Station’s Cloud Cover -4
In the satellite observations segment of cloud cover determination for a station, radiance changes measured by satellites are interpreted using climatic models’ algorithms.
For the case study station satellites 3-D cloud data are obtained from A- Train satellites, figure 5. Data from CLOUDSAT, CERES, TERA-AQUA-MODIS, CALIPSO, SRB and ISCCP satellites were downloaded and processed. Analyses of each set of satellite data were carried out and their output charts displayed in figure 6 are used for corroborating the surface visual cloud cover result.

## Slide 18
Figure 5: A – TRAIN SATELLITES

## Slide 19
Figure 6: OTA [CU] CLOUD COVER AND THE CORROBORATING SATELLITES OVER IT

## Slide 20: Station Radiometric Data Acquisition
In an observation station at least one radiometer will be required for radiometric data collection, and radiosonde data or satellite radiometric data will be needed for corroboration.
In the Ota – CU station case study, 9103 Spectrum Analyser is in use; fifty - three years radiosonde observations data was acquired, filtered and extracted to obtain each cloud layer’s values for the required primary parameters – pressure (hPa), temperature (K) and calculated geopotential height (m).

## Slide 21
Figure 7: 9103 Spectrum Analyser Outdoor Unit

## Slide 22
Figure 8: 9103 Spectrum Analyser Indoor Unit with PC

## Slide 23: Station Radiometric Data Analysis
Attenuation distribution and statistics for each of the eight listed cloud models were computed from the processed radiosonde data.
The station logged spectrum analyser data (SPAD) were extracted and analysed under two conditions - rainy and non-rainy days, using the climatological device’s monthly data for each year.
Then all the processed data for three years were integrated and the integrated data cumulative distribution curve obtained.

## Slide 24: Station Radiometric Data Analysis - 2
Each distribution curve is a result of raw data processing using electronic spread sheet programming to implement several layers of required station conditions such as geographic, climatic and spectra conditions. The resulting cloud attenuation cumulative distribution curves at 12.5 GHz for each of the existing cloud models and that for the spectrum analyser data (SPAD) were compared in figure 9.

## Slide 25
Figure 9: SPAD and Cloud Models Distribution Curves at 12.5 GHz

## Slide 26: Cloud Attenuation Modelling
The SPAD integrated attenuation cumulative distribution curve approximates a straight line of slope - 0.31011 and intercepts 3.089 dB, which appear as a resultant constructive interference of some pairs of periodic functions of comparable amplitudes. A possible general mathematical representation of these observations is equation (1):
Ac (WL, θ, t, f) = f(x) = acos(x) + bsin(x) = Acos(x – α) (1)

## Slide 27: Cloud Attenuation Modelling - 2
where A = (a2 + b2)1/2 and α = tan-1(b/a) in the range 0 < α < π/2; considering the variables of the cloud attenuation (Ac) - cloud liquid water content (WL) of each cloud layer series (CLS) and their temperature (t); angle of elevation (θ) and frequency (f) of propagating radio signals; x is considered to be cloud layer specific attenuation coefficient (KL) defined in the International Telecommunication Union Recommendation (ITU-R) P.840 – 4, corresponding to the frequency function g(f) in the Salonen – Uppala procedure [6].

## Slide 28: Cloud Attenuation Modelling - 3
Considering the relatively gentle slope of the SPAD line, the range of x should be 0 to π rather than 0 to π/2, and using the straight line analogue, a = - 0.31011, b = 3.089 dB, as directly measured from the graph; A = 3.08915 and α = - 1.560796 by computation; hence the equation (1) becomes:
Ac = 3.08915WLCOS ((0.5KL) + 1.560796)
0 KL π (2)

## Slide 29: Cloud Attenuation Modelling - 4
Situations of constants and constant variable parameters of the equation having more than one possible form or value are resolved by generating the distribution and chart corresponding to each of the most probable options. The option whose chart is closest to that of the station measured data distribution (SPAD) is taken.

## Slide 30: Cloud Attenuation Modelling - 5
Then the proposed model i.e. equation (2) is tested by comparing its performance with those of the standard cloud models at the station as shown in Figures 10 – 14.

## Slide 31
Figure 10: Cloud Attenuation Models Distribution Curves at 12.5 GHz

## Slide 32
FIGURE 11: OTA – CU CLOUD MODEL Vs FOUNDATION MODELS AT 12 GHz

## Slide 33
FIGURE 12: OTA – CU CLOUD MODEL Vs FOUNDATION MODELS AT 14 GHz

## Slide 34
FIGURE 13: OTA – CU CLOUD MODEL Vs FOUNDATION MODELS AT 20 GHz

## Slide 35
FIGURE 14: OTA – CU CLOUD MODEL Vs FOUNDATION MODELS AT 30 GHz

## Slide 36: Cloud Attenuation Modelling - 6
Hence equation (2) represents the cloud attenuation model for the station having shown considerable geometric pattern agreement with the foundation models at various frequencies.

## Slide 37: Future Work
Radiometric measurements, cloud visual data and climatological data acquisition need to start and continue in every climatic zone of Nigeria, i.e. about every state of the federation, particularly in high tele-density areas as Lagos state, to enable development of relevant hydrometeors’ models and corresponding cloud attenuation statistics.
However, a single global satellite based climatic model is desirable, where modular algorithm would be used to integrate the various climatic zones models.

## Slide 38: References
[1] Das S, Chakraborty S and Maitra A, (2013): Radiometric measurements of cloud attenuation at a tropical location in India; Journal of
Atmospheric and Solar-Terrestrial Physics, (105-106): 97-100.
[2] Eva R I, Gustavo A S, Jose M R, and Pedro G P, (2015): Atmospheric Attenuation in Wireless Communication Systems at Millimeter and THz Frequencies; IEE Antenna and Propagation Magazine, 57 (1): 48- 61.
[3] Omotosho T V, Mandeep J S and Mardina A, (2013): Cloud Attenuation Studies of the Six Major Climatic Zones of Africa for Ka and V Satellite System Design; Annals of Geophysics; 56 (6): 1-2.
[4] Gerace G C and Smith E K, (1990): A Comparison of Cloud Models; IEEE Antennas and Propagation Magazine.
[5] Warren, S. G. and Hahn, C. J. (2002): Climatology; Encyclopedia of
Atmospheric Sciences, Academic Press.
[6] Salonen, E. and Uppala, S. (1991): New prediction method of cloud attenuation; Electron, Lett 27, 1106-1108.

## Slide 39
T H A N K S